## Slide 1
SI CCS Flow

## Slide 2: Overview
paper: A robust cell-level crosstalk delay change analysis
Victim Driver output response
Victim Receiver input response
Victim Receiver output response
Normal delay
Aggressor responses(current + voltage)
Select alignment
Victim Driver output response(consider aggressor current)
Victim Receiver input response(consider aggressor voltage)
Victim Receiver output response
SI delay
delta delay

## Slide 3: Why receiver output?
ROP(receiver-output probing)

## Slide 4: Overall Flow
filter aggressor+建RC mesh
ROM
计算各aggressor到vic driver的注入电流
计算各aggressor到vic sink的bump
计算vic normal delay
计算各aggr window ratio
各vic sink
align aggressor
各align point
计算vic si delta delay
siCCS::UpdateXTCCSDelayNormal

## Slide 5: GenMesh
siMT.cpp: lpNetRLC* netRLC = GetSI()->GetTd()->GetNetRLCWithXcap(net, ck);
拿到vic的RC信息。
vicDriver
vicSink1
vicSink2
RC tree only with coupled node
filter aggressor+GenMesh:
vicDriver
vicSink1
vicSink2
coupled RC tree
lpRLCNode上的cap值为对地电容与耦合电容之和。
lpRLCCouple记录耦合点。
AggrDriver1
AggrDriver2
AggrSinks
加入了aggressor的RC信息。
这里不考虑二次耦合。

## Slide 6: Normal delay计算
1. 生成vic driver input波形，再solve ccb解出vic driver output波形；
2. vic driver output波形通过卷积计算得到sink pin波形；
3. sink pin波形再去解ccb的到sink out波形，并得到normal delay。
source
sink

## Slide 7: 计算注入电流
Replacing k-th aggressor driver with corresponding voltage source and short-circuiting all other drivers.
vicDr
aggDr
rc
rc
n1
n2
n3
vic driver不连接电容时，计算到n1, n2, n3三点的电压(卷积)，再分别除以r1, r2, r3得到电流波形后相加。
r1
r2
r3
vicDr
rc
若vicDr有连接电容，为方便测量注入电流，在建mesh后会加一小电阻。
vicDr
rc
n1
n1
计算aggr到n1的电压，除以r1的到电流。
r1

## Slide 8: 计算bump
Replacing k-th aggressor driver with corresponding voltage source and short-circuiting all other drivers.
aggDr
rc
rc
n1
n2
n3
r1
r2
r3

## Slide 9: align
vdd
0.9vdd
0.5vdd
t1
t2
t3
rise max

## Slide 10: SI delay计算
1. normal delay时生成的vic driver input波形，考虑注入电流，solve ccb解出vic driver output波形；
2. vic driver output波形通过卷积计算得到sink pin波形；
3. sink pin波形叠加aggressor bump；
4. 再去solve ccb的到sink out波形，并得到si delay。
source
sink
+

## Slide 11
THANK YOU
WWW.GIGA-DA.COM
电话：0755-61018899
邮箱：info@GIGA-DA.COM
邮编：518000