## Slide 1
打造完整的国产芯片数字EDA平台
A Quick Look at RTL Synthesis
Daisy Li 2024/05/07

## Slide 2
01.
Digital IC design flow
03.
Synthesis - translate
05.
Synthesis - optimize
02.
RTL synthesis flow
04.
Synthesis - timing constraints
06.
Synthesis - output data

## Slide 3: Digital IC Design Flow
图源：来自网路

## Slide 4: What Synthesis Do?
synthesis = translation + logic optimization + gate mapping
translate (read Verilog, vhdl, sverilog)
optimize + map
RTL Source
residule = 16’h0000;
if (high_bits == 2’b10)
residue = state_table[index];
else
state_table[index] = 16’h000;
Generic Boolean Gates
GTECH, unmapped format
Constraints
set_max_area ...
create_clock ...
set_input_delay ..
Technology Specific Gates
Mapped format

## Slide 5: RTL Synthesis Flow
Load designs and libraries
Apply timing constraints
Synthesize the design
Write out design data
Create setup file
RTL Verilog, *.v
Liberty file, *.lib
Create constraints file
Timing constraints
Environmental attributes
Select appropriate compile flow
Export files for physical design
Gate-level Verilog netlist
Constraints, *.sdc
SCAN-DEF.def
Translation
Optimization
Mapping

## Slide 6: RTL Synthesis Flow
Load designs and libraries
Apply timing constraints
Synthesize the design
Write out design data
Create setup file
RTL Verilog, *.v
Liberty file, *.lib
Create constraints file
Timing constraints
Environmental attributes
Select appropriate compile flow
Export files for physical design
Gate-level Verilog netlist
Constraints, *.sdc
SCAN-DEF.def
Translation
Optimization
Mapping

## Slide 7: Verilog File
Gate-level ，结构化描述
RTL, 数据流描述
行为级描述
Reference:
https://zhuanlan.zhihu.com/p/458300788
https://blog.csdn.net/yinjian0924/article/details/125246107

## Slide 8: Translate
module TOP (A,B,C,D,CLK,OUT1);
input A, B, C, D, CLK;
output [1:0] OUT1;
wire INV1, INV0, bus1, bus0;
ENCODER U1 (.AIN (A), ... , Q1 (bus1));
INV U2 (.A (BUS0), .Z (INV0));
U3 (.A (BUS1), .Z (INV1));
REGFILE U4 (.D0 (INV0), .D1 (INV1), .CLK (CLK));
endmodule
Design
Clock
Port
Net
Pin
Cell
Reference
INV
INV
ENCODER
REGFILE
CLK
D0
D1
Q[1: 0]
U4
U1
U2
U3
INV0
INV1
AIN
BIN
CIN
DIN
A
B
C
D
CLK
Q0
Q1
OUT[1: 0]
TOP
Design
Clock
Port
Cell
Net
Pin
Reference

## Slide 9: RTL Synthesis Flow
Load designs and libraries
Apply timing constraints
Synthesize the design
Write out design data
Create setup file
RTL Verilog, *.v
Liberty file, *.lib
Create constraints file
Timing constraints
Environmental attributes
Select appropriate compile flow
Export files for physical design
Gate-level Verilog netlist
Constraints, *.sdc
SCAN-DEF.def
Translation
Optimization
Mapping

## Slide 10: Timing Constraints
K
S
N
Q
D
D
Q
Q
QN
QN
FF2
FF3
T
M
D
Q
QN
D
QN
FF1
FF4
A
MY_DESIGEN
KOBE’S_DESIGEN
KING’S_DESIGEN
CLK
All input paths are constrained by set input delay.
All register-to-register paths are constrained by create clock.
All output paths are constrained by set output delay.

## Slide 11: Constrain Register-to-register Paths
create_clock -period 2 [get_ports CLK]
Default Clock Behavior:
Clock rise at 0ns and has a 50% duty cycle;
Zero rise/fall transition time;
Zero skew
Zero insertion delay or latency
Max allowable delay for the reg-to-reg path “K”: 2ns-0.2ns
0ns
1ns
2ns
K
S
N
Q
D
D
Q
QN
QN
FF2
FF3
A
MY_DESIGEN
CLK
Tsetup, FF3=0.2ns

## Slide 12: Model Clock Skew
K
S
N
Q
D
D
Q
QN
QN
FF2
FF3
A
MY_DESIGEN
CLK
Tsetup, FF3=0.2ns
create_clock -period 2 [get_ports CLK]
set_clock_uncertainty -setup 0.14 [get_clocks CLK]
Max allowable delay for the reg-to-reg path “K”:
2-0.14-0.2ns
0ns
1ns
2ns
0.14
0.2

## Slide 13: Model Latency or Insertion Delay
Q
D
QN
CLK
3ns
1ns
origin of clock
source latency
network latency
create_clock -period 2 [get_ports CLK]
set_clock_uncertainty -setup 0.14 [get_clocks CLK]
set_clock_latency -source -max 3 [get_clocks CLK]
set_clock_latency -max 1 [get_clocks CLK]

## Slide 14: Model Transition Time
0ns
1ns
2ns
transition
create_clock -period 2 [get_ports CLK]
set_clock_uncertainty -setup 0.14 [get_clocks CLK]
set_clock_latency -source -max 3 [get_clocks CLK]
set_clock_latency -max 1 [get_clocks CLK]
set_clock_transition 0.08 [get_clocks CLK]

## Slide 15: Constrain Input/Output Paths
K
S
N
Q
D
D
Q
Q
QN
QN
FF2
FF3
T
M
D
Q
QN
D
QN
FF1
FF4
A
MY_DESIGEN
KOBE’S_DESIGEN
KING’S_DESIGEN
CLK
create_clock -period 2 [get_ports CLK]
set_clock_uncertainty -setup 0.14 [get_clocks CLK]
set_clock_latency -source -max 3 [get_clocks CLK]
set_clock_latency -max 1 [get_clocks CLK]
set_clock_transition 0.08 [get_clocks CLK]
set_input_delay -max 0.6 -clock CLK [get_ports A]
set_output_delay -max 0.8 -clock CLK [get_ports B]
B

## Slide 16: Environmental Attributes
Apply environmental attributes to model timing effects of:
  Input drivers and transition time
  Output load capacitance
  PVT operating conditions or corners
  Interconnect parasitic RC: WLM
create_clock -period 2 [get_ports CLK]
set_clock_uncertainty -setup 0.14 [get_clocks CLK]
set_clock_latency -source -max 3 [get_clocks CLK]
set_clock_latency -max 1 [get_clocks CLK]
set_clock_transition 0.08 [get_clocks CLK]
set_input_delay -max 0.6 -clock CLK [get_ports A]
set_output_delay -max 0.8 -clock CLK [get_ports B]
set_input_transition 0.12 [get_ports A]
set_load 0.03 [get_ports B]
set_link_library “xxx_slow_proc.lib”
set_operating_conditions -max rcworst
set_wire_load_model -name xxx

## Slide 17: RTL Synthesis Flow
Load designs and libraries
Apply timing constraints
Synthesize the design
Write out design data
Create setup file
RTL Verilog, *.v
Liberty file, *.lib
Create constraints file
Timing constraints
Environmental attributes
Select appropriate compile flow
Export files for physical design
Gate-level Verilog netlist
Constraints, *.sdc
SCAN-DEF.def
Translation
Optimization
Mapping

## Slide 18: Optimize
RTL Description
Architectural
Logic-level
Gate-level
Optimized Netlist
Performs three levels of optimization:
  Architectural-level or high level optimization
  Logic-level or GTECH optimization
  Gate-level or mapping optimization
Tries to mimimize area while meeting timing and other constaints
Arithmetic optimization:
  Constant/operant folding: A+2*B-2+B-A+7  3*B+5
  Common sub-expression sharing:
    Z1=A+B+C; Z2=C+D+B  T=B+C; Z1=A+T; Z2=T+D
  SOP -> POS transformation: A*C+B*C (A+B)*C
  Parallel constant multipliers optimization:
    105=64+32+8+1, 621=105+512+4
load splitting and logic duplication
Boundary optimization
Test-ready synthesis, scan chain
Adaptive retiming

## Slide 19: Optimization Examples
1-load splitting & logic duplication
2-boundary optimization
3-test-ready, scan chain
4-adaptive retiming

## Slide 20: Generate Timing Report

## Slide 21: RTL Synthesis Flow
Load designs and libraries
Apply timing constraints
Synthesize the design
Write out design data
Create setup file
RTL Verilog, *.v
Liberty file, *.lib
Create constraints file
Timing constraints
Environmental attributes
Select appropriate compile flow
Export files for physical design
Gate-level Verilog netlist
Constraints, *.sdc
SCAN-DEF.def
Translation
Optimization
Mapping

## Slide 22: Q&A
Always 对应什么样的电路？
if...else.. 对应什么样的电路？MUX如何实现的？
output *.sdc：基于用户设置的constraint, 输出mapping之后更准确合理的sdc
综合最终关注哪些指标？
综合阶段如何考虑功耗
  SPEF, VCD?
  wire model如何给？WLM来源？
  Synthesis目前仅考虑leakage; 也能基于vcd考虑动态功耗；

## Slide 23
THANK YOU
WWW.GIGA-DA.COM
电话：0755-61018899
邮箱：info@GIGA-DA.COM
邮编：518000

## Slide 24: Digital IC Design Flow
设计规格
Design Specification
HDL硬件代码
RTL Coding
逻辑综合
Logic Synthesis
DFT实现
Scanchain/Mbist
自动布局布线
Auto Place & Route
时序，功耗/压降签核
Timing, Power/IR Signoff
流片
Tape-out
ASIC设计与实现
参考模型
Reference Model
功能仿真
Design Verification
DFT验证
功能验证
形式验证
Formal Verification
门级仿真
Gate Simulation
形式验证
Formal Verification
后仿
Post-Gate Simulation
版图验证
Physical Verification
速度
Frequency
低功耗设计
Low Power Design
功能时序约束
Design Constraints
综合时序报告
Synthesis Report
性能指标
功耗
Power
静态时序分析
Pre-layout STA
静态时序分析
place/CTS/route STA
静态时序分析
Post-layout STA
功耗分析
Power Analysis
低功耗约束
UPF
低功耗实现
Low Power Flow
前
端
后
端
工艺库
逻辑库
物理库
芯片架构规格书