## Slide 1: Paper Sharing Guidelines
Author list here
Paper introduction by your name
Add numbers to
Trace questions

## Slide 2: Agenda
Background
Proposed Solution
Experiment Result
Takeaway Notes
Reference

## Slide 3: Background of your paper
Good problem introduction solves 70% work
Jitter means delay variation:
Jitter will impact chip design timing performance
Jitter is impacted by power supply noise
If jitter is too large, your design will fail!
Question: How to handle jitter(delay variance) introduced by power supply noise?
What is the problem?
What is the novelty?
What is the contribution?
What is the key idea?
What is the impact?
Example:

## Slide 4: Previous work
1. Traditional allowable drop too small, (e.g. 5% VDD)
Number is much more convincing!!!
How fast is fast?
How do you define better?
2. Remember to add reference information*
for main points
Why previous work failed? Disadvantages?
* Yujeong Shim and Dan Oh, Impact of Dynamic Power Supply Noise Induced by Clock Networks on Clock Jitter and Timing Margin

## Slide 5: Challenge
Why difficult?
Why this problem is not solved before?
Why this method / solution is necessary?
Use figures, tables to explain!
Switch dip
Result in overdesign

## Slide 6: Objective/solution, Top-down flavor
How to solve it? In TOP-DOWN flavor
Main target/model
Sub module 1
Sub module 2
Start point
Step 1
Step 2
Conclusion
Otherwise,
audiences get confused

## Slide 7
Ask yourself:
    What is the assumption?
    What is the hypothesis?
    What is not discussed?
Solution explanation
Check by yourself:
    One page one topic
    Terminology is unified
    Unit is not missed
    Y-axis, x-axis is marked, explained
    Acronym is explained
    Font > 20pt
    Use simple English!
    Time control, rehearsal!

## Slide 8: Experiment Result
Memory controller ASIC block
Designed to run at 800MHz
The data path setup delay is 1.25nsec
Sensitivity is about 3.5ps/mV.
The clock path delay is 0.7nsec
Sensitivity is linearly scaled from the data.
Predict over 10ps jitter
Predict 1ps jitter
Use DC sensitivity function
(sensitive to high frequency noise)
Over pessimistic
New approach
Target impedance approach
Setup:
Smaller jitter under power noise is predicted.
Result:
Explain result
Conclusion

## Slide 9: Takeaway Notes: (optional)
Jitter means delay variation, impacted by power noise
Higher voltage -> less delay
Lower voltage -> longer delay
Large voltage droop only have little jitter impact.
Tracking effect, period jitter
Use sensitivity to predict jitter under power noise.
General relationship between jitter and noise:
Sensitive to power noise at middle-low frequency (<0.1 f_clk)
Not sensitive to power noise at high frequency (> f_clk)

## Slide 10: Useful Reference: (optional)
Keng L. Wong, Tawfik Rahal-Arabi, Matthew Ma, and Greg Taylor, Enhancing Microprocessor Immunity to Power
Supply Noise With Clock-Data Compensation
Dan Oh and Guang Chen, Challenges and Solutions for Core Power Distribution Network Designs
Yujeong Shim and Dan Oh, Impact of Dynamic Power Supply Noise Induced by Clock Networks on Clock Jitter and Timing Margin
Yujeong Shim and Dan Oh, System Level Modeling of Timing Margin Loss Due to Dynamic Supply Noise for High-Speed Clock Forwarding Interface
Dan Oh, Supply Noise Induced Jitter Modeling and Optimization for High-Speed Interfaces
Guang Chen and Dan Oh, Improving the Target Impedance Method for PCB Decoupling for Core Power
Dan Oh and Yujeong Shim, Power Integrity Analysis for Core Timing Models

## Slide 11: Appendix (optional)

## Slide 12
Q & A