## Slide 1: IncPIRD: Fast Learning-Based Prediction of Incremental IR Drop
Chia-Tung Ho and Andrew B. Kahng
CSE and ECE Departments, UC San Diego, La Jolla, CA, USA
Paper introduction by Jiaxiao Qin

## Slide 2: Agenda
Background
IncPRID
Experiment Result
Conclusion

## Slide 3: Background
When instance output is rising.
VDD will charge the load.
Cause VDD IR drop
t
VSS baunce
Similarly, if load is falling
Energy is dumping to VSS
Cause VSS IR baunce
t
t
VDD (IR drop)
I
(Power delivery network)

## Slide 4
Why we need to care IR drop?
If too much IR drop,
Timing impact (slower)
Function error
Typically max 10% VDD
t
t
VDD (IR drop)
I

## Slide 5
How to model IR drop
Engineering changing order
We need to solve a huge matrix!
Since numerous time-consuming iterations among PDN design, fast and accurate incremental IR prediction has emerged need.

## Slide 6: IncPRID(Incremental Prediction of IR Drop)
Original design information (DEF, LEF; golden tool power pad file, GSR file, Technology file)
IR drop report file;
Current distribution
Incremental modification by designer (macro/cell block movement or change ; modification of the PDN to have a denser grid; adding/moving power pad
(Golden tool)
IncPRID
Model
Static IR drop of each power node that has tap current source attached

## Slide 7: Training Flow
Use KVL, KCL, branch equations and
superposition to efficiently extract
relevant electrical features.
Use XGBoost as machine learning model
(Golden tool)

## Slide 8: Prediction Flow
Constraints come from
robustness experiment, when
break the constrains, the error
would be large

## Slide 9: Experiment
Experimental Setup
  In C++ with LEF/DEF reader/writer parsers
  On a 2.6Ghz Intel Xeon Dual-CPU server with 256GB RAM
  150 SOC floorplan designs(80% training data and 20% testing data)
  RedHawk as golden tool

## Slide 10: Experiment Result
Model accuracy experiment

## Slide 11: Experiment Result
Incremental IR Prediction experiment
Perform one incremental modification.
Separately perform modifications of macro and cell block, power pads, and intermediate metal layer track usage.

## Slide 12: Experiment Result
Chain incremental modifications
(i) change the power of one cell
block from 10mW to 100mW,
(ii) move a macro,
(iii) add a power pad, and
(iv) use denser intermediate
metal layer

## Slide 13: Experiment Result
Robustness of model

## Slide 14: Experiment result
Model accuracy on different designs
To test the ability to predict IR drop in new designs without retraining model.
Most of the test designs with prediction error larger than 5mv do not satisfy the constraint1.

## Slide 15: Conclusion
The approach can handle modifications of macro/cell block locations, PDN structure, and power pads and predict IR drop.
achieves 22-1000X speedup compared to RedHawk with average error less than 1mV and maximum error around 5mV.

## Slide 16: Q&A

## Slide 17: Thanks for listening!