## Slide 1
Power
Analysis
Basics III

## Slide 2
Outline
Basic knowledge
Signal probability
Switching activity
Reference on paper

## Slide 3
An ASIC Low Power Primer: Analysis, Techniques and Specification
Leakage power
from subthreshold leakage / gate-oxide tunneling /
/ reverse biased junction leakage
Output pin switching power
load capacitor charging/discharging
estimate / extract switching activity
glitch generation and propagation
Input pin internal power
PMOS and NMOS both turn on (T_overlap is overlap time)
caused by crowbar current/ overlap current.
short curretn larger if rise time is slow (large slew)
input pin switch but output does not switch
input pin switch, output pin switch
Must
Read!

## Slide 4
How to get power of a cell?
Report_power_analysis [get_cell an_and_gate]
VDD
VSS
Y
A
B
C
Cell power =
Leakage power
+ Internal power
+ Switching power
Sum of: State-probability * state-leakage-value
Switching probability (toggle rate) and lookup table
Alternatively, get from .lib default value (fast, but NOT accurate at all!)
In .lib file
From VCD/ SAIF annotation
And propagation altorithm
From extraction or wire/cell model

## Slide 5
Require 1: power value in .lib
Internal power table in .lib
inverter A triggered internal power
related to input transition and
output cap
Leakage power
state dependent value

## Slide 6
Require 2: signal probability and switching activity
By annotation or propagation
VDD
VSS
Y
A
B
C
Annotation method
run simulation, generate VCD for each wire
convert to SAIF, then annonate to net
Propagation method
We only know the input vector
Extract SWA from input pin
Propagate to entire whole chip
extract_toggle_activity
get_toggle_activity_pins
report_toggle_activity
set_toggle_activity
In many cases:
We have some annotation information
Need to propagate to other nets
Input
vectors
0
1
…
1

## Slide 7
Require 3: load capacitance, VDD level, and so on…
Load capacitance from RC extraction, or .lib, or estimation
VDD from scenario, setting, .lib
We also need timing support (reason in later slides)
These details will not be discussed in this PPT

## Slide 8
How GIGA run report_power_analysis?
// UI entrance
taTclReportPowAnnCmd::Eval
powMgr::CalcInstPower
PowMgr::CalcInstPower(dbInst*)
GetInstSDCPower ()
CalcAvgInternalPow
CalcAvgSwitchingPow
CalcLeakagePow
Direct use lib default power value?
No, for VP analysis purpose.
Yes, for fast optimization purpose.
Get defautl leakage power from lib
Or calculate State dependent leakage power
dbInst::GetAvgLeakagePower()
check signal probability, then use lib data
Check the switching activity of input pin
Then calculate using lib lookup table
powMgr::CalcInternalPow
Check switching activity
Check load capacitance
Then calculate switching power
CUDD
Symbolic
algorithm
Switching Activity
Algorithm
Calculation signal probability
Glitch pattern
Logic difference…
Propagate signal propability from input to output

## Slide 9
Outline
Basic knowledge
Signal probability
Switching activity
Reference on paper

## Slide 10
Signal probability (requried by leakage power)
Example, P(Y) waves has same signal probability. (similar as duty ratio)
Several difinations… Suppose x(t) (or x[n]) is the signal value (1 or 0 ) at time t ( or clock cycle n)
P(x) means, for a clock cycle (or a given time):
What is the probability of wire x == 1?
if P(x) == 1 , wire x is always 1
if P(x) == 0, wire x is always 0

## Slide 11
Then internal nodes can be propagated as this:
= p1+p2-p1p2
Suppose input vectors (VCD or test bench for example), we cancluate P(x) as follows
Extract and propagate signal probability
Can we propagate P(x) now?
Fanout-reconvergent problem.
Even original input is SSS, local P(x) propagation can fail.

## Slide 12
No! Local P(x) propagation can over or under estimate !!!
P(A)
…
…
P(AAAAAAA…) = P(A)
Since signal logic exponent can not exist
P(A)
P(B)
P(AB)
P(ABB) = P(AB)
Therefore, we
supress exponent in expression
Example: suppose we want to calculate the signal probability of
Calculate minus is awkward…
Notes: Question: see low power cmos vlsi , page 73. z = x x’…

## Slide 13
…
Any expression can be expressed as
Sum of input products
The P(x) is combinatino of
“and” / product, “xor” / sum
How to supress and deduce P(x) effectively?
First: We know any logic function f(x1, x2, x3…..) can be convert to sum-prod format

## Slide 14
Then use BDD (binary decision diagram) to supress exponents
Then ab +c can be expressed as BDD form based on Shannon’s expansion:
Deep first transverse to find out (ab+c) signal probability
P(a’)P(c’)0 + P(a’)P(c)1 + P(a)P(b’)P(c’)0 + P(a)P(b’)P(c)1+P(a)P(b)1
= P(a’)P(c) + P(a)P(b’)P(c) + P(a) P(b)
0
1
1
0
1
0

## Slide 15
a
b
0
1
a+b
Giga use CUDD to build BDD, and propagate P(x)
https://davidkebo.com/cudd
https://davidkebo.com/verilog-binary-decision-diagram-parser
Some other BDD examples for logic functions

## Slide 16
Anlib/anlibcell.cpp
Db/dbProject.cpp
Db/dbGroupCells.cpp
Db/dbBool.cpp
Db/dbLibCell.cpp
Db/dbSocv.cpp
Db/dbLibPin.cpp
Db/dbScope.cpp
Fe/feBddBdd2Ptrs.h
feTcl/feTclInit.cpp
feTcl/feTclHelp.doc
Pow/powGlitch.h
Pow/pow.h
Pow/powUtil.cpp
Sch/schSymbolCG.cpp
Sch/schSymFFGenerator.cpp
Sch/schSYmbol.cpp
Sch/schSymLatchGenerator.cpp
Ta/ta.h
Ut/utGV.h
Xe/
Get BDD tree here
Find out how BDD (CUDD package) is used in GIGA products
Propagate P(x)
Get glitch pattern
(logic patters that will trigger glitch)
Logic equivalance check
(verification)
Logic optimization
And so on…

## Slide 17
Your task:
Read through CUDD link and example
study how to build a node, and evaluate logic table.
Grep “EvalProbability” in work/src/db/dbInst.cpp
explain how CUDD is used in leakage calculation?
dbInst::GetAvgLeakagePower()
Where you can get state leakage power?
How you get state probability , P(x)?

## Slide 18
Outline
Basic knowledge
Signal probability
Switching activity
Reference on paper

## Slide 19
What is signal probability, toggle rate,
switching activity, transition density…
Signal probability (SP) The average fraction of clock cycles in which the steady state value of the node 𝑥 is a logic high.
Switching Activity (SWA) / transition density If a logic signal 𝑥(𝑡) makes ) transitions in a time intervals of length 𝑇, then the switching activity of 𝑥(𝑡) is defined as :
Normalized transition density
A wire X is 0 or 1
P(x) is the probability x is 1 in a clock cycle.
P(x) = 1 means wire x is always 1
P(x) = 0.5 half of the time, wire is 1
How many transitions (0->1 or 1->0)
Per second?
How many transitions in a clock cycle

## Slide 20
Signal probability {P(x)} and transition density {D(x)} example
Example, P(Y) is equivalent in both case (50%) for case 1 and case 2
But transition density is different!
D(y) in case 1 is 2X larger than case2!
case 1 has much higher dynamic power than case 2!
case 3 and case 2 has same D(y), but P(y) is different. Leakage is different.
D(x) of a clock is 2f: for each clock cycle, clock toggles twice.

## Slide 21
Switching activity/ transition density/ toggle rate is very complex
We need to estimate SWA to calculate dynamic power!
Case 1: Functional switch:
A input pin switched, cause Y switch
1
0->1
0->1
If a input pin switch,
And the switch can pass to output
Then output pin can switch
*1991_Najm_Transition delay, a new measure of activity in digital circuits.pdf

## Slide 22
Wait, what is boolean difference?
Deisnty propagation problem:
Means X switches can impact output y
X is transfer to y
Y(x) + Y(x’) = yx’ + y’x
CUDD / BDD can help on this

## Slide 23
Switching activity/ transition density/ toggle rate is very complex
We need to estimate SWA to calculate dynamic power!
Case 2: Simultaneous fake switch. Case 1 is over-estimated
1->0
0->1
No switch!
What if 1 pin switches
What if 2 pin switche simultaneously
……..
Whst if n pin switche simultaneously
Now consider two pins switch
The propability this switch is propatated to output
Only one pin switches
Must be zero. Why?
Switching prpb. At out

## Slide 24
Normalized activity/ the probability of x switching in current cycle
Zero!!!

## Slide 25
If xi xj trans from 00 to 11
Or trans from 11 to 00
Cause y switches
Remove half, because
00 -> 11 can not happen contineously.

## Slide 26
How GIGA calculate functional switching

## Slide 27
Note: n input switch simtinously
Can be very rare, therefore ignore

## Slide 28
Switching activity/ transition density/ toggle rate is very complex
We need to estimate SWA to calculate dynamic power!
Case 3: generated glitch
1->0
0->1
If input pins are glitch pattern.
And edge is wider than arc delay
Then output glitch happen!
Glitch propagation probability
Wider than arc delay
How many glitch switch at output per second
Glitch rate:
How many glitch pattern can generated per second
Determined by gate type and frequency (Again BDD!)

## Slide 29
Glitch rate 1997 Lim paper consider arc delay. Delay can filter glitch.
The switch probability in a clock cycle is D(a)/f
The rising probability is (D(a)/f)/2
Non-switching pins, and they are biased to a value
So that glitch can be propagated to output
Generated glitch probability in a clock cycle
Glitch rate: how many glitch patterns can generated per second

## Slide 30: How to get glitch rate in GIGA?
is the probability that non-toggle inputs are biased such that the glitch can go through the gate.
Apply Boolean differential operation between output pin and two input pins in the glitch pattern
  NAND gate example: Y = ABC
  NOR gate example: Y = A+B+C
  XOR gate example: Y = A C
  = , force 1
CUDD gives you glitch patterns, and evaluate probabilities
“other_input_pins” in code
“all_input_pins” in code

## Slide 31
The probabilty that glitch can pass…
If a glitch pattern is generated.
The edge of a and b arrives at random value α, β
Then | α – β | must > τ, then glitch can pass.
The probability of this is :
Edges are too close
Shorter than arc delay
Glitch is filtered
GIGA needs timing update to get
Arrive time range

## Slide 32
Total transition rate
(switching activity
How many toggle edge per second)
D(x), transition density. Probability of transition in a clock.
How many functional transition per second.
1st proposed in 1991_Najm
2nd removed simutaneously switch in 1994_Chou
3rd improve calculation efficiency in 1994_Kappor
Pattern P: Some pattern can generate glitch.
Prppagate P: The pattern input events shall wider than arc delay
Proposed in 1997_Lim
A glitch can pass from previous input.
Proposed in 1999_hashimoto
A glitch means one rising and one falling
Glitch can overlap or close with eachother. (insufficient interval)
Direct add will result in over estimation.
Hashimoto 1999 set a low boundary (assume other pin do not switch during propogating glitch
Giga uses “side SWA scale factor”
If other pin does not toggle, the prop glitch go through as Hashimoto 1999
if other pin toggles, then :
if other pin toggle will heavily impact prop glitch, B = 1
else, other pin toggle will not impact prop glitch, B = 0.5 (default)
  parameter glitch_power_side_swa_scale_factor, default value 0.5

## Slide 33
Your task:
1. Search work/src/pow. Find out where GIGA calculate switching power?
Run a report_power_analysis QA case.
Set breakpoint on below functions.
What is call stack? How GIGA uses these API?
CalcPropagatingGlitchPow()
UpdateAnnGlitchRate()

## Slide 34
Reference:
Find out in wiki!

## Slide 35
All other pins are not in the pattern,
And biased in the logic level, which can pass the glitch generated
By pattern
The probability of pattern happens

## Slide 36
Our optimization method consists of two techniques; a statistical
estimation method of glitch activities and an optimization
algorithm for gate resizing. For the estimation of glitch activities,
we classify glitches into two classes; generated glitches and propagating
glitches. As for the generated glitches, we adopt a statistical
estimation method proposed by Lim and Soma[8]. The propagating
glitches, however, are not considered in their method, and therefore
we have devised a statistical estimation method. The optimization
algorithm has been designed to have the ability of escaping from a
bad local solution while keeping small computational costs.
1999 hashimoto

## Slide 39
Inter connection aware glith propagation
Glitch reduction optimization
https://ieeexplore.ieee.org/document/1432125
https://ieeexplore.ieee.org/document/7124828