## Slide 1: Resistance Analysis and Report

## Slide 2
Report resistance for one cell
Set_app_var ir rc_mode2
Set_app_var ir rc_keep_pg_only true
analyze_pg_resistance -net VDD
report_pg_resistance –net VDD cellName
How to debug resistance value?
Report_pg_rc –net VDD –layer M1 –length 6.5 –width 0.08
Resistance: 0.0317482 (Kohm)
Capacitance: 0.000432064

## Slide 3
effVDDRes, minVDDPRes
effVSSRes, minVSSPRes
+
=
combinedEffRes
combinedMinPathRes
What is combined Resistance

## Slide 4
V=0
V=0
Why adding source node will improve eff res
Min Path resistance: find shortest path from graph
Effective resistance: get equivalent resistance from cell to supply location

## Slide 5
在用户侧： set_power_network_mode -reset #set_power_network_mode -supply_param "VDD 0.99 VSS 0" #set_power_netowrk_mode -nets "VDD VSS"
report_misc -min_resistance min_path_res.rpt report_misc -effective_resistance effective_res.rpt
当前实现：
analyze_pg_resistance use script to merge resistance from two files in report, the script will dump "instance name VDD VDDres VSS VSSres totalRes" table
Then combined PG is done by python
Expectation (default is min path resistance) analyze_pg_resistance -output_combined_report min_path_res.rpt analyze_pg_resistance -effective -output_combined_report effective_res.rpt