## Slide 1: ESD Models, Devices and Analysis

## Slide 2
Topics
ESD event and models
ESD protection devices
TLP and device characterization
ESD analysis

## Slide 3
ESD Events and Models
ESD, electrostatic discharge, occurs between two bodies of different electrostatic potentials
ESD has short duration between 0.1ns to 100ns
ESD has high current pulse, 1A to 30A
ESD has high voltage, hundreds to thousands of volts
To fight against ESD event
  Proper grounding during manufacturing and handling
  Use ESD protection circuits

## Slide 4
What Are We Protecting
Device junction, requires high voltage to damage
MOS gate oxide, requires relatively lower voltage to damage
Thermal and EM, requires high current to damage
Good protection means large ESD devices and large capacitance which affect circuit performance
  High performance IO requires careful design
System level may need external ESD devices

## Slide 5
ESD Events and Models
There are many ESD models correspond to different scenarios
  HBM
  MM
  CDM
  System level ESD stress (Gun Test)

## Slide 6
Human Body Model (HBM)
This model corresponds to the discharge of a charged human being into the IC
Capacitance is 100pF, body skin resistance is 1.5K
The requirement is between 2KV to 8KV

## Slide 7
Machine Model (MM)
This model corresponds to the discharge of a charged (assembly)machine into the IC
Capacitance is 200pF, resistance is only few ohm
The requirement is few hundred volts
There is strong relationship between MM and HBM

## Slide 8
Charged Device Model (CDM)
This model corresponds to the discharge of a charged IC to GND
CDM event is very short, rise time less than 0.5ns, high current of tens of Amp
Mostly causes gate oxide failure
The requirement is few hundred volts

## Slide 9
ESD Models

## Slide 10
System Level ESD Stress (Gun Test)
This model corresponds to “real world” discharge when user handles the product
Stress level is much higher and applied to all exposed surface of the product
First peak is short similar to CDM, second peak is similar to HBM with higher stress

## Slide 11
ESD Protection Devices
Diodes
GGNMOS, grounded gate NMOS, snap-back
SCR, snap-back
Big FET
Self protection, silicide block

## Slide 12
Diodes
Diodes are used in forward bias to conduct large ESD current
Has no effect in reverse bias, except capacitance affect circuit performance
Simulation not accurate due to model issue

## Slide 13
GGNMOS
GGNMOS, grounded gate NMOS, uses snap-back

## Slide 14
Silicon Controlled Rectifier (SCR)
SCR uses latch-up like mechanism to achieve snap-back
Has lower snap-back hold voltage than GGNMOS
Most effective, however, there is latch-up concern

## Slide 15
BigFETs
BigFETs is a large NFET between VDD and GND, triggered and controlled an RC circuit and inverter chain
The time constant needs to avoid accidental turn on by power up

## Slide 16
Transient Voltage Suppressor (TVS)
System level ESD requirements are higher than chip level, 8KV vs 2-4KV
External ESD devices can be used together with internal ESD, it’s also called TVS

## Slide 17
What is CDM Clamp
CDM event requires its own circuit to deal with the main issue, fast rise time
  Failure is gate oxide break down, keep gate voltage low

## Slide 18
IO

## Slide 19
IO

## Slide 20
TLP and ESD Devices
ESD tests only give pass/fail, no device I/V characteristics
Transmission line pulse (TLP) is used to obtain device I/V characteristics
A trapezoidal positive current pulse is applied to DUT
The current and voltage through the DUT are measured and produce the I/V characteristics
The DC leakage of the DUT is also measured to determine pass/fail
The commonly used pulse is Tr=10ns, Tw=100ns, data taken at 90ns

## Slide 21
TLP and ESD Devices

## Slide 22
TLP and ESD Devices

## Slide 23
TLP and ESD Devices

## Slide 24
TLP and ESD Models
TLP 100ns current pulse is equivalent to HBM stress
A good correlation between TLP It2 value and HBM fail level
  2KV HBM failure will also fail 1.33A TLP, 1.5kVHBM / ATLP
HBM and MM also correlates well
  2KV HBM corresponds to 100V MM, 20 times
IEC gun test and TLP stress
  1A TLP corresponds to 600V IEC
  13.3A TLP for 8K IEC

## Slide 25
ESD Analysis
To simulate ESD event, we needs
  The model of the ESD current pulse, available
  The model of all ESD devices and circuitry connected and affected
    ESD device models come from characterization at test wafer
    Circuitry connected and affected by ESD event
      Different ESD event goes through different path
    Parasitic of the connection, ESD results highly dependent on parasitic values, resistance value at few ohm, require accurate RC extraction
  Can be simulated with regular circuit simulator
  Snap-back behavior can’t be simulated

## Slide 26
ESD Analysis

## Slide 27
ESD Analysis

## Slide 28
ESD Analysis

## Slide 29
导师：代用名
电子信息科学与技术203班
电子信息夺学院
深圳鸿芯微纳技术有限公司
2022/7/12