## Slide 1
IR drop
Analyze, Solve,
& Validation

## Slide 2
Outline
IR drop background knowledge
Solve IR drop with sparse matrix
IR drop validation method

## Slide 3
Floorplan
Main tasks…
Decide core shape and size
Place big macros and fix them
Place IO pads, PG pads.
Distribute PG rings/straps
(roughly distribute small cells.)
Challenges
A lot of information is unknow, chicken-egg dilemma
Avoid routing congestion around macros.
Initial floorplan need to “predict” future timing.
PG distribution impacts future cell placement…

## Slide 4
Graph to represent PG network
Source node:
Supply node, bump, pad
Act as voltage source
Middle node:
Power stripe
Power rings
Target node:
Connect to instance
Millions of instance…
Similar structure goes to VSS PG network
PG routing on different layers.
With parasitic resistance and capacitance
Pad/PG port
bump
Supply loc

## Slide 5
Why dynamic IR drop happens?
t
t
VDD (IR drop)
I
t
VSS bounce
When instance output is rising.
VDD will charge the load.
Cause VDD IR drop
Similarly, if load is falling
Energy is dumping to VSS
Cause VSS IR baunce
“0”
“1”
“failed”

## Slide 6
Why we need to care IR drop?
t
t
VDD (IR drop)
I
If too much IR drop,
Timing impact (slower)
Function error
Typically max 10% VDD

## Slide 7
How to model IR drop
bool irPGMgr::ExtractPGraph will extract RC
Of PG network. (Work/src/ir/irMgr.cpp)
Inst. Rise/fall is modeled by current source.
Charging and discharging is model by load cap
~
~
~
~

## Slide 8
IR drop types:
~
~
~
~
If use average current: ( + + ) / VDD
Static IR drop analysis
If use worst simutinous switch
Dynamic vector-less
IR drop analysis
t
I
If use actual switch current (e.g. from VCD)
Dynamic vector based IR drop analysis
 | Pros | Cons
Static IR drop | Very fast. Find high resistance hot spot | Can not fix dynamic drop (e.g. switching current)
Vector-less dynamic IR drop | Middle. Find dynamic drop | Too pessimistic
Vector based dynamic IR drop | Slow. High accuracy. Find actual dynamic drop | Need many input vectors (huge VCD file)
For details:
Check manual
Analyze_power_network

## Slide 9
最后，VP进行IR仿真后，为了估计VDD/VSS波动对于某个instance的时序影响，需要获得timing window中平均/最坏/最好的 (VDD-VSS)，分别用 efftw, mintw, maxtw。如果仿真若干个周期，那么整个周期最坏/最好的 (VDD-VSS)用 minwc, maxwc表示。在vector-based 仿真中，实际的instance的翻转期间（switching window），可能远远小于timing window，甚至落在timing window之外。则在switching window中，最好/最坏的（VDD-VSS）分别用 max_switching_win，min_switching_win 表示。这些概念如下图所示。
[DTH] display mintw, efftw, maxtw, minwc, maxwc min_switching_win, eff_switching_win, max_switching_win for dynamic IR drop map
For each cell, we have minwc
Dynamic IR
From .lib
Simplified wave
Dynamic I terminology

## Slide 10
Vector-based switching
Actual switching time
http://10.30.200.21:8088/projects/hongtu-emir/wiki/Simulation VCD comes from..
http://10.30.200.21:8088/projects/hongtu-emir/wiki/Cutting_edge_paper_sharing ATPG, sim, GPU acc.
Dynamic I switching window, arr Win

## Slide 11
Worst case switch
Vector-less
Dynamic I switching window, arr Win
(vector-less)

## Slide 12
How to prepare static I & (R -> G)?
PG routing on different layers.
With parasitic resistance and capacitance
Each cell has power
Power/VDD = I_avg
|-> P_leak (SP + .lib)
+ P_sw (SWA + C)
+ P_internal ( SWA + .lib + twf + C )
|-> C from spef (Xu)
|-> SWA from SAIF/VCD
PG network has parasitic resistance
source design.rlc
VDD
VDD
pnode
pedge
pnode
pnode
pedge

## Slide 13
See rlc files for details
http://10.30.200.21:8088/projects/hongtu-emir/wiki/Resistance_and_capacitance_calculation_method

## Slide 14
The overall static IR flow chart…
PG structure
spef
twf
VCD
SAIF
Power data
Supply location
ploc
rlc
IR analysis
Current
Compose_top_design
DEF
LEF
TECH
EM analysis
package
Source node
Middle node
Target node
sp
Ploc
mapping

## Slide 15
The overall usage flow
Compose_top_design $top_def $blk_def $tf_file $lefList
Import_lierty
Link_project
Source $rlc_file
Import_parasitics
Source $ploc_file
Import_twf
Extract_switching_activity
Report_power_analysis
set_power_network_mode
analyze_power_network
report_power_network
report_misc -static_ir
emirTcl/emirTclIRDrop.cpp
emirTcl/emirTclUtil.cpp
Etc/python/utility/customized_report.py
The overall testing flow
ut/test/ut/vp/ir/static_ir
qa_analyze_power_network
qa_report_power_network

## Slide 16
Known (high priority) static IR issues to begin with…
客户的脚本无法检查到static IR 波动 (6mV tolerance too large)，需要增强qa_xx 引入tolerance 设置，红区比对
Static IR drop ticket 需要建立regression
李军建立的 case suite，需要覆盖相应的regression
代码重构解耦注释
现有 static ir case 仅有30个，其中 10个是换solver的重复功能测试
有效测试用例 20 个。
目标：
1/20 之前，扩充到 50 个 case
1/30 扩充到 100 个 case（对不同的case 做static IR，试不同的flow）
1/30 能解 10 个相关的 ticket
奖金：

## Slide 17
TBA

## Slide 18
db
Graph
包含了 static 右端项
(从db power中获得）
irDynaSim
APM
ta
动态的右端项电流
irCurrCap.cpp

## Slide 19
irDynaSim
Solver
irPGraph
irPGMgr::SolverDynaSimVector()

## Slide 20
Trapezoidal in time domain:
  G*(Vn+1+Vn) +2C/h*(Vn+1-Vn) =In+1+In
  (G+2C/h) Vn+1 = (In+1+In) + 2C/h*Vn - G*Vn
  h is time step. Again, solve Ax = b
Bypass method
V 不变，且 I 不变 within tolerance
  (In+In-1) + 2C/h*Vn-1 - G*Vn-1
  (In+1+In) + 2C/h*Vn - G*Vn
  (In+1 - In-1) + (2C/h - G) (Vn - Vn-1 )
1. In+1 In-1 (0.001mA)
2. Vn Vn-1 (0.0001V) 0.1 mV

## Slide 21
字典映射信息
Net1 -> aaax
Net2 -> bbbc
数字信号的翻转信息
#100
1aaax
1bbbc
….
#190
0aaax
0bbbc
#200
0aaax
0bbbc
Net1
Net2
#100
#190

## Slide 22
Outline
IR drop background knowledge
Solve IR drop with sparse matrix
IR drop validation method

## Slide 23
irPGMgr ->
irDynaSim (vecor, vectorless)
irPGMgr::_pGraph
irSolver
Static IR: G V = I
Dynamic IR: C (dV/dt) + G V = I
Solve IR drop on each PG network node whole flow…
AMD + LDL
irPGMgr
Static current: db-> (power) -> 建立 pGraph的时候存在node上
Dynamic current: irDynaSim ->
graph2matrix

## Slide 24
~
Why sparse matrix solver???
I
R
Question:
We know the I (from .lib)
We know the R (from PG extraction)
Would it be nice if we direct calculate IR drop by:
V = R I ?
Nope. Because:
R is too dense (many non-zero values)
Large R calculation is expensive (two nodes are not connected)
Dimension is huge (million level)
Solution:
We save matrix for G = 1/R.
Hence, we have:
G V = I
Benefits:
Many zeros in the matrix (see blanks)
Many methods to solve sparse matrix
…
…

## Slide 25
Basic Sparse Matrix Solve Method
Target: we know the G and I.
We want to solve:
G V = I
So that:
V = I
Traditional method is VERY expensive!
We use LU partition to solve matrix (L: low left triangle. U: upper right triangle)
Suppose we want to solve L x = y
X can be solved iteratively from x1 to xn
=
Suppose we want to solve U x = y
Take a guess, how to solve this?
=

## Slide 26
Basic Sparse Matrix Solver, core algorithm
If G matrix is positive definite (R is possitive ) G can be factorized as:
G =
To solve G V = I is to solve L U V = I
We firstly solve (let UV = y)
L y = I
Then we solve
U V = y
However:
LU factor can generate many non-zeros (nnz) in the triangle area
“fill-in” challenge
Huge computation cost
Task 1: (Use python or anything…)
I dump a G matrix (dim 1015340 (middle + target) nnz 3263938)
    need to visualize the matrix, validate in Matlab

## Slide 27
Advanced Sparse Matrix Solver, core algorithm
We are using L D L’ = G to reduce fill-in effect
We even use AMD + LDL to speed up solving
      P’LDL’P = G
Here P is permutation, PP’ = element matrix.
AMD is to swap columns and lines to reduce fill-in
To Solve Ax = b
Is to solve P’LDL’P x = b
1. LDL’ (P x) = (P b)
2. (Px) = (Pb) / (LDL’)
3. x = P’ ( (Pb)/ (LDL’) )
Checkout irSolve.cpp
bool irPGMgr::LDLSolve(bool bUseDynaPeakCur, irPGraph *subGraph)

## Slide 28
Short summary:
IR drop analyze is to solve G V = I
G dim is million level, and sparse
Now we use LDL’ or AMD+LDL’ to factorize G into
      P’LDL’P = G
      Then solve P’LDL’P V = I iteratively
We are looking for even faster and larger cap solver
(e.g. multi-thread solver)
Actually I hide MANY detailed algorithms.
If you are interested in this topic, do let us (Xu Luo) know!

## Slide 29
Now we want to solve dynamic IR
R
…
…
~
Trapezoidal in time domain:
  G*(Vn+1+Vn) +2C/h*(Vn+1-Vn) =In+1+In
  (G+2C/h) Vn+1 = (In+1+In) + 2C/h*Vn - G*Vn
  h is time step. Again, solve Ax = b
Transient simulation core function
Dynamic IR: C (dV/dt) + G V(t) = I(t)
1. C(dV/dt) + G V_n = I_n
C(dV/dt) + G V_(n+1) = I_(n+1)
3. dV/dt = (Vn+1 – Vn) / h
*Proof flow is contributed by Xu Luo
irDynaSim -> Solver -> I/V -> I(n+1) -> Solver -> I/V
Notes: Will add a very tiny cap (min_cap) on each nodes, so that the matrix property can be greatly improved.

## Slide 30
Transient IR drop simulation
In irSolve.cpp::SetupLDL (Gp, Gi, Gx, Cg, I, incSrc, subGraph) // line 960
  For each target node, node->GetI()
  For each middle node, node->GetI()
  For each source node, node->GetCapOnNode()
  For each middle node, node->GetCapOnNode()
  For each target node, node->GetCapOnNode()
  Foe each node in the pGraph, node set small minimal cap
Used by vector / vector-less dynamic IR simulation
irDynaSimLinear::DynaSim
irDynaSim.cpp:1264
PrepareGPlus2Ch() // then factorize
RetriveInew(t) // get call back value of I(n+1)
ComputeIx() // // Target:Ix = (I1 + I0 + 2*Cg/h* V0) - G*V0
ComputeVnew() // LDL solver…
ComputeTHnew() // do nothing
ForwardStepVars() // idDynaSIm 1389
Build PG network
irMgr::_pGraph
Extract RC of graph
Add current and cap to node
SetupLDL
Fill in G, C, I into solver
Run transient simulation

## Slide 31
Outline
From circuit to matrix solving
(Nodal analysis, Modified Nodal Analysis)
Matrix solving basics

## Slide 32
Nodal analysis is a stamping method
If we know the structure of circuit
We can directly write matrix （stamping）
eliminate KCL, KVL, etc.
Super suitable for static IR analysis
1. 主对角线 = 所有分支电导之和
2. 非对角线 = 分支电导相反数
3. 如果挂载电流源，设为右端项
Property: SPD
1. 对称的 (电阻没有方向性）
2. 正定的 (即 U’ G U >=0
纯电阻网络只会消耗能量）
3. 实际中，对角元大于该列（行）的非对角元和的绝对值，就能确保正定性*。
Gershgorin 圆盘定理： 对称阵主对角元为正占优必正定
U = I R
G U = I
G = 1/R
I^2 R >=0
C U’ +

## Slide 33
Need to cleanup graph
Check graph is valid

## Slide 34
Modified Nodal Analysis
Nodal analysis has limitations…
1. How to model inductance?
2. How to model voltage source?
3. How to model controlled source? (VCCS, CCCS, VCVS, CCVS)
Modified Nodal Analysis provide extension based on Nodal Analysis.
Lay the foundation of SPICE simulation engine.
Transient Nodal Analysis
Nodal analysis also support cap stamping.
This is giga used for dynamic IR analysis today.
Will add content later…

## Slide 35
Solving all the voltage (ir drop) in a circuit is to solve:
G V = I
Fundamental problem (this is pure math problem):
1. is there exists solution?
2. is solution unique?
The remaining is merely engineering problem 

## Slide 36
Suppose two-dimension space.
Ax = b has solution means
Find a cross point of two lines:
=
By scaling and rotation x1 x2 of two lines
(you can actually try to drag above group in ppt),
we can somehow solve A:
=
If two lines (vectors of matrix A) can not span a space, then solution may not exist
=
?
If two lines are linearly dependent, then infinite solutions
=
G V = I
G is SPD
Means unique solution exists!
G is singular
Oops…

## Slide 37
Very simple method for 2 or 3 dim matrix
Expensive, too many computation
A direct method to get accurate result
Gaussian Elimination Method
=
=
=
=
If pivot (枢轴）is obtained
We can simply stretch x2, and get solution
Pivot (枢轴）

## Slide 38
Gaussian Elimination Method n-dim space
=
=
0
=
0
0

## Slide 39
Solve matrix by LU decomposition
Target: we know the G and I.
We want to solve:
G V = I
So that:
V = I
Traditional method (Gaussian method) is VERY expensive!
We use LU partition to solve matrix (L: low left triangle. U: upper right triangle)
Suppose we want to solve L x = y
X can be solved iteratively from x1 to xn
=
Suppose we want to solve U x = y
Take a guess, how to solve this?
=
Forward Elimination
Backward Substitution

## Slide 40
Basic Sparse Matrix Solver, core algorithm
If G matrix is positive definite (R is possitive ) G can be factorized as:
G =
To solve G V = I is to solve L U V = I
We firstly solve (let UV = y)
L y = I
Then we solve
U V = y
However:
LU factor can generate many non-zeros (nnz) in the triangle area
“fill-in” challenge
Huge computation cost
Task 1: (Use python or anything…)
I dump a G matrix (dim 1015340 (middle + target) nnz 3263938)
    need to visualize the matrix, validate in Matlab

## Slide 41
When fill-in happens?
=
=
0
Will generate many fill-ins
If bottom right is relatively dense
Caused by gaussian elimination

## Slide 42
When fill-in happens?
=
=
0
Much less fill-in on the right part
Of U matrix

## Slide 43
When fill-in happens?
=
=
0
=
=
0
Reordering can reduce fill-in

## Slide 45
Iterative Methods

## Slide 46
Build PG network
irMgr::_pGraph
Extract RC of graph
Add current and cap to node
SetupLDL
Fill in G, C, I into solver
Run transient simulation
Export SPICE
And I
Run SPICE
simulation
VP agrees with SPICE?
Now we can dump out PG network in SPICE format
I can also dump out I and V from VP simulation
Task 2:
We want to check, if SPICE result correlates with VP?
Step 1:
Verify static IR drop
Step 2:
Verify vector-based IR drop

## Slide 47
module load ngspice/26
ngspice some_circuit.sp
ngspice
IT helped to install ngSPICE. (since ngSPICE supports mixed-signal and verilog-A)
Please let me know if you want other SPICE simulator
You can find more example usage from ngSPICE homepage
Or /home/stor19d2p1/jchen2/folks_case/jx_static_ir/rc_test.sp
ngSPICE support four kinds of analyze mode
.op operating potint analysis (stable v, for static IR drop analysis)
.dc dc sweep analysis .dc srcnam vstart vstop vincr
.tran tstep tstop transient analysis (for dynamic IR drop analysis)
.ac dec nd fstart fstop AC analysis

## Slide 48
Static IR drop analysis
/home/stor19d2p1/jchen2/folks_case/jx_static_ir
You can check the static IR drop using script : test_static_ir.tcl
PG network SPICE model: pg.sp
SPICE static IR drop result: static_ir_result
You can run:
ngSPICE pg.sp
In the ngSPICE shell run:
-> op
To perform static IR analysis
(takes 8797.436 seconds.)

## Slide 49
Target node, node id and coor
In the GUI, I found 5mV drop
ngSPICE dump voltage of node
Node 1 is very close to 1.075
Primilarly check using ARM A5, 1.08 VDD result

## Slide 51
To start with…
Setup a very simple pg network ( for example, 4X4 PG network, with four current source)
Run the ngSPICE, and try to extract voltage drop for each node.
Try to dump out target node (instance voltage drop ) from VP.
(You can check report_power_network)
If anything is missing, please let me know, I can enhance.
Try to compare worst static voltage drop, difference? Relative error?
Try to compare the voltage drop node-by-node, error, deviation, correlation, etc.

## Slide 52
Dynamic IR drop analysis
/home/stor19d2p1/jchen2/VP_QA_base/QA_designs_v2/ARM_tiny_case
A very tiny case with 400 instance (target nodes)
tiny_arm.tcl Read design, link
tiny_sim.tcl script to perform simulation, generate VCD
tiny_arm_pg.tcl script to create power network (you can modify and try)
tiny_arm_stage2.tcl analyze static, dynamic v-less, v-based IR drop
tiny_arm_dynamicir/ dynamic IR analysis result directory
pg.sp SPICE netlist of power network. Current source is “average current”
pg_current.sp Current value of each target node + middle node
pg_voltage.sp voltage drop value of each target node + middle node

## Slide 53
To start with…
Write a script to parse pg_current.sp, pg_voltage.sp
Try to draw waveforms for a node.
Replace current source in pg.sp, replace with pwl source.
The pwl source can be extracted from pg_current.sp
Measure the volage drop value on each target node.
Measure the max dynamic voltage drop on each target node.

## Slide 54
Modify PG structure, and check Irdrop (1)
/home/stor19d2p1/jchen2/VP_QA_base/QA_designs_v2/ARM_tiny_case
In tiny_arm_stage2.tcl, suppose the static IR drop of VDD is shown in below.
After testing the correlation of static IR drop and dynamic IR drop.
We can also test the PG network shape impacts on IR drop. (narrower PG, larger IR drop)
Then, if we down-size the power rail width, we should see larger IR drop.
Please refer to tiny_arm_stage3.tcl for reference.
In the script, I modify the rail width from 0.3 to 0.2 (compare tiny_arm_pg3.tcl and tiny_arm_pg.tcl)
You can see the IR drop becomes larger.
Please modify the pg parameter, and
perform more correlation check.

## Slide 55
Modify PG structure, and check Irdrop (2)
How to generate new data?
Use customized AG build: /home/jchen/work_stor19d2p1/jchen2/dyna_build/AG
Source tiny_arm_stage2.tcl
the vector-based IR drop analysis will generate SPICE netlist and waveform
perform correlation check
Modify tiny_arm_pg3.tcl , source tiny_arm_stage3.tcl
run vector-based IR drop to generae new SPICE netlist and waveform
perform correlation check
More details on PG structure can be found in manual:
http://172.168.8.15:8088/projects/aguda-techpub/wiki/Aguda_user_guide