## Slide 1: XGraph data member related.
_mNodeList metal list
_vNodeList via list
_bin[layerIdx] store all nodes to bin, for search overlapped objcts.

## Slide 2: Extract XGraph
CreateNodeLists
net set（-net ）
isGenrateSupplyLoc (default : true)
DB
Iterate dbPath( design has secondary PG pin route),
add wire and via to metal node List
and via node list separately .
(For via with large scale of cuts, each cut will be treated as one node )
Iterate dbShape ( all routed rectangle object ), add wire and via to metal list and via list separately.
Iterate all partition ‘s cells, iterate dbPath and dbShape for metal node and via node.
_mNodeList (irXNode)
_vNodeList (irXNode)
_bin[layerIdx] (guBin)
_mNodeList (irXNode)
_vNodeList (irXNode)
_bin[layerIdx] (guBin)
Has bug here, param rail has redundancy pin here for adding node
_mNodeList (irXNode)
_vNodeList (irXNode)
_bin[layerIdx] (guBin)
UsePortPhyPin(default false)
Iterate all port, add metal objects and via objects to node list separately, and set type as PHYS_PIN_RECTS.
_mNodeList (irXNode)
_vNodeList (irXNode)
_bin[layerIdx] (guBin)
CreateSrcNodes

## Slide 3: Extract XGraph
CreateSrcNodes
CreateSrcNodeAtBumps
Iterate All Bumps(COVER CELL) ‘s ports.
Create supply point at port pin geometry which overlapped with metal or via objects.
Add supply point to list in each layer.
CreateSrcNodeAtPads
Iterate all power pad (POWER PAD CELL) ‘s cell pin geometry which overlapped with metal or via objects.
Add supply point of overlapped area to supply list in each layer.
UsePortPhyPin(default false)
Iterate all physical pin
Add pin via as source node if has.
Add supply location at pin end as source node
Transfer supply point into source node. And add to search bin in each layer.
_srcPtList[layerIdx]
_srcPtList[layerIdx]
_srcPtList[layerIdx]
_bin[layerIdx] (guBin)
_mNodeList
FlattenMacroPadPG
Iterator instance pin which has library “PNA_LIB”, add pin intersect area with current node list to node list.(PHYS_PIN_RECT)
What’s “dbLibrary::PNA_LIB” ?
_mNodeList(irXNode)
_vNodeList (irXNode)
_bin[layerIdx] (guBin)

## Slide 4: Extract XGraph
MergeOverlapXCNode
Iterator metal nodes and merge overlapped middle node on same metal layer
_mNodeList (irXNode)
_bin[layerIdx] (guBin)
CreateEdges
Merge overlapped via nodes in each cut layer.
_vNodeList
_bin[layerIdx]
For metal node in each layer, create edge between overlapped geometries. If head node is supply point, edge box will be supply point box. Otherwise, overlapped area is set to edge box. And via box overlapped this node in adjacent cut layer will be also set an edge.
For via node, create edge between via nodes in adjacent cut layer. Edge box is the intersect box between via nodes.
_mNodeList (irXNode)
_vNodeList (irXNode)
_bin[layerIdx] (guBin)
_vNodeList (irXNode)
_bin[layerIdx] (guBin)
CreateCurrSrcLocations
(Find all target node here)
Add pad pin which has overlapped via/metal node in adjacent layer to node list with type PHYS_PIN_RECT.
Create Edge between physical pin and overlapped node (not supply point or pin node).
Edge box is overlapped bounding box.
And flag node/edge to leaf cell pin
dbPnaModel::WHITEBOX ?
_mNodeList (irXNode)
_vNodeList (irXNode)
_bin[layerIdx] (guBin)

## Slide 5: Extract XGraph
CreateECOEdge
For metal node on adjacent layer, create ECO edge between current metal and overlapped metal above layer. When there is no object for via insertion.
_ecoEdgeList
For metal nodes on each 2 adjacent metal layer, create edge between metal node when there is enough area to insert via pillar.
_ecoEdgeList

## Slide 6: Extract PGraph
ExtractPGraph
_xGraph
_lpMgr:
irParam
_powApi
Iterator via node in xGraph,
for each via xnode, create pnode (point) on each xedge (center). And set pnode as client to xedge.
Foreach via pnode, create pedge between via metal pnodes which has shortest distance. And set via xnode as client to this pedge.
pedge is an rectangle based on two pnodes (point).
(set voltage on pnode, and user area,unitR, num cuts on pedge)
Supply type : 1
_edgeList
_nodeList
_srcNodeList
_midNodeList
_TgtNodeList
For std cell instance which attached with power rail, create pnode at each pin rectangle center, and set current on each pnode.
Iterator metal node’s xedge.
Create pedge if both two xedges adjacent of xnodes have pnode as client.
Set width (2) and g to pedge.
And set c (half of wire c) to each pnode on current pedge.
Pedge’s box is a line between two point
Supplytype: 2