## Slide 1: Self-heating Effects
Daisy Li
2021/09/24

## Slide 2: Device Self-heating
∆TFEOL=Rth * P
  Rth: thermal resistance of instances, ℃/mW; (provided by Foundries)
  P: total power of instances, mW.
Calculating through FEM
  ∆TFEOL=Tile-based ∆T

## Slide 3: Metal Self-heating
∆TBEOL =α * β * ∆TFEOL+ ∆TRMS
  α: metal connecting/overlapping effects;
    α connection – metals being directly connected to IO pin;
    a overlapping – metals crossing over instances.
  β: thermal coupling effects;
    β = C1 * ∆TFEOL + C2 * ∆TRMS + C3
  ∆TRMS = ∆TRMS_margin * ()2
  α connection/overlapping, C1, C2 and C3 are provided by Foundries.
Calculating through FEM
  ∆TBEOL = Tile-based ∆T + ∆TRMS

## Slide 4: References
Stephen H. Pan, & Norman Change. (2015). Fast Thermal Coupling Simulation of On-chip Hot Interconnect for Thermal-aware EM Methodology.
http://www.chinaaet.com/article/3000107393