## Slide 1: SI for Free: Machine Learning of Interconnect Coupling Delay and Transition Effects
Keywords: Signal integrity(SI), incremental transition time, incremental delay, SI-aware path delay, machine learning
Andrew B. Kahng , Mulong Luo and Siddhartha Nath
ECE and CSE Departments, UC San Diego, La Jolla

## Slide 2: Outline
Introduction
Related works
Modeling methodology
Experiments
Conclusions

## Slide 3: Background (for myself)
Why SI?
  In nanometer technologies, the noise can impact in terms of functionality or in terms of timing of the devices.
  The crosstalk noise refers to unintentional coupling of activity between two or more signals.
  This results in switching activity on a net to cause unintentional effects on the coupled signals.
Signal integrity plays an important role in the deep submicron technologies.

## Slide 4: SI mode vs. non-SI mode
Accurate signoff timing analysis: use SI mode in signoff timing tools.
81ps
Path slack in SI Mode (ns)
Path Slack in Non-SI Mode (ns)
The path slack can differ by up to 81ps between SI and non-SI analyses.
Path slack divergence in SI and non-SI analyses with clock period 1.0ns, as reported by a commercial timer in 28nm FDSOI technology.

## Slide 5: However…
  High STA licenses fees:
      The cost of one license of a timing tool with SI mode analysis enabled is typically several times the cost of a default (with no SI analysis capability) license.
  Long runtime:
      The runtime for SI-aware timing analysis on the top-10K paths can be up to 3 longer than the runtime of non-SI analysis on designs.

## Slide 6: In this work
  Use ML-based predictors of timing in SI mode based on timing reports from Non-SI mode.
  SI analysis without SI tools.
    Save money
    Save runtime
    Get accuracy
Non-SI timing report
Machine learning predictors
SI timing report
Post P & R Database

## Slide 7: Main Challenge: non-SI to SI
Several electrical, logic structure, and layout parameters;
Complex interactions between parameters;
Commercial STA tools is a black-box;
…
Example:
Path slack variation with clock period;
Arc delay and incremental transition time variation with ground and coupling capacitances.
Commercial STA tools

## Slide 8: Contributions
Analyze multiple sources of timing divergence between non-SI and SI mode;
Develop 2 new machine learning-based models for incremental transition time and delay due to SI;
Accuracy and robustness of models.

## Slide 9: Related works (I)
Analytical SI delay models:
1. Sapatnekar (2000)
  Lumps coupling capacitance to ground with Miller coupling factor;
  Uses an iterative algorithm to estimate the crosstalk delay on net.
2. Xiao (2000)
  Derive a two-pole model for RC interconnect noise waveform calculation with coupling capacitance.

## Slide 10: Related works (II)
Correlation of STA tools:
1. Thiel (2004)
  Correlate SPICE to PT timing reports.
2. Kahng (2013)
  Minimize the gap between internal incremental STA tool and signoff timing tool;
  Use least-squares regression to estimate wire delay.
  3. Han (2014)
  Use deep learning models to correlate SI to SI and non-SI to non-SI timing between STA tools.
2. + 3. = Non-SI to SI with non-linear model!

## Slide 11: Modeling methodology
(i) Selection of parameters that affect incremental delay in SI mode;
(ii) Application of nonlinear modeling techniques to capture the complex interactions of parameters
Several electrical, logic structure, and layout parameters

## Slide 12: Selection of parameters
Rw x Cc
Incremental Delay in SI Mode (ns)
LE
Incremental Delay in SI Mode (ns)
Rw is the resistance of an arc
Cc is the coupling capacitance of an arc
LE is the logic effort of a driver

## Slide 13: More parameters
Correlations between the selected parameters and the result exist.
Non-linear correlation.
More parameters are needed.

## Slide 14: Modeling parameters
incremental delay in non-SI mode;
transition time in non-SI mode;
clock period;
resistance;
coupling capacitance;
ratio of coupling-to-total capacitance;
toggle rate;
number of aggressors;
ratio of arc’s stage to the total number of stages;
logical effort of driver;
the differences in max (min) arrival times of the signal at the driver’s output pin for the victim and its strongest aggressor.
“Our experimental results indicate that dropping any of the parameters can reduce the modeling accuracy by at least 5%.”
Sources from SPEF, non-SI report, library and SDC files.
Several electrical, logic structure, and layout parameters

## Slide 15: Model
Electrical, logic structure, and layout parameters and constraint
Incremental transition time due to SI
Incremental delay due to SI
SI-aware path delay

## Slide 16: Modeling flow
Linear regression cannot capture complex interactions between parameters.  non linear model
60% for training, 10% for validation and the remaining 30% for testing
188K data points of nets

## Slide 17: Modeling flow: ANN
One input and one output.
Two hidden layers. Each hidden layer has up to twice the number of neurons as the number (24) of input parameters (12).
Five-fold cross validation to avoid overfitting.

## Slide 18: Modeling flow: SVM
Radial Basis Function (RBF) kernel / Gaussian kernel
Gamma value: the inverse of the number of the parameters
Five-fold cross validation to avoid overfitting

## Slide 19: Modeling flow: HSM
A. B. Kahng, B. Lin and S. Nath, “Enhanced Metamodeling Techniques for High-Dimensional IC Design Estimation Problems”, Proc. DATE, 2013, pp. 1861-1866.
Use Hybrid Surrogate Modeling (HSM) to combine the predicted values from the ANN and SVM models and obtain the final predictions.

## Slide 20: Experimental setup
illustration of an artificial testcase
Key parameters swept in experiments

## Slide 21: Experiment I : Accuracy
Worst-case absolute error of 7.0ps (8.8%)
Range of errors is 11.3ps
Average absolute error of 0.7ps (0.6%)
Incremental transition time prediction
Black line: ideal correlation
Red circle: experimental data points

## Slide 22: Experiment I : Accuracy
Worst-case absolute error of 5.2ps (15.7%)
Range of errors is 9.8ps
Average absolute error of 1.2ps (1.1%)
Incremental delays Prediction
Black line: ideal correlation
Red circle: experimental data points

## Slide 23: Experiment I : Accuracy
Worst-case absolute error of 8.2ps (6.9%)
Average absolute error of 1.7ps (1.4%)
SI-aware path delays Prediction

## Slide 24: Experiment II : Robustness
New implementation of jpeg_encoder signed off with different clock period, and utilization.
Different Cc, Rw, driver size and other parameters…
“unseen” data point
Worst-case absolute error is 7.0ps (12.3%)
Average absolute error is 1.6ps (2.6%)
Training set
Validation set
Testing set
“Unseen” data

## Slide 25: Conclusions
Non-SI to SI: Cost and runtime savings for SoC design.
Analysis of electrical, logic structure and layout parameters that cause timing in non-SI mode to diverge from that in SI mode.
Provide a machine learning-based methodology that can accurately model incremental delay due to SI, and SI-aware path delay. (And more accurate than previous work.)

## Slide 26
Thanks!

## Slide 27
Backup

## Slide 29: Models of Han (2014)
Actual SI-aware path delays, versus predicted path delays using models of Han
How to improve?