## Slide 1
ngSPICE
Engine

## Slide 2
ngSPICE
spicelib
devices
Up to bsim4 v7
parser
analysis
misc
Malloc,
data structures
math
Sparse solver
Derivitive
Fft
Poly…
Frontend, command line

## Slide 3
Download source code
git clone https://git.code.sf.net/p/ngspice/ngspice download_dir
Ubuntu install Dependency
autoconf (suto apt-get update; suto apt-get install autoconf)
libtoolize (suto apt install libtool)
automake (already installed)
yacc lex (sudo apt-get install flex bison)

## Slide 4
Install binary and shared library
    Make release directory
    Cd to release
    ../configure --with-ngshared --prefix=PATH/bin/
    will do check and copy necessary files into release/
Only install binary (No need to install adms)
    $ ./autogen.sh
    $ mkdir release
    $ cd release
    $ ../configure --without-x # new env doesn’t fully support X11
    $ make
    $ sudo make install
See /rnd/jchen/ngspice34/ for example pre-compiled ngspice

## Slide 5
How to link with static library (for fast run-time purpose)
Step 1: include head file in source code
Step 2: suppose shared lib is complied as libngspice.so
option 1 :export LD_LIBRARY_PATH=/lib:/usr/lib:/usr/local/lib
option 2 : under local directory
gcc main.c -Wall -s -lngspice -lpthread -ldl –L. -o ./bin/Debug/ng_sh
-s remove symbol table
-l add static link library between lib, and so.
-L add link library search path
Double click to download lib example

## Slide 6
Search more options for gcc
Option Index - Using the GNU Compiler Collection (GCC)
configure、 make、 make install 背后的原理(翻译) - 知乎 (zhihu.com)
More backgrounds on compile flow