## Slide 1
Low Power Flow & UPF

## Slide 2
Low power background story
Low power 1: the logical diagram, power domain
Low power 2: the physical implementation
floorplan
power net, power region
power management cell
Low power 3: design rule check
UPF support
Agenda

## Slide 3
Case study…
Suppose we want to design a SPARC processor with low-power capability
(only focus on core logic, cache, MMU are not in scope)
Let’s refresh processor pipeline diagram…
Instruction
cache
tlu
if
dc
ex
fx
ls
Data
cache
Low power design target:
Floating point unit: requires high-speed, high-voltage, can be shut-down.
Execution unit: bottleneck of pipeline, requires high-speed.
Other part of pipeline: can run with low-voltage to save power.
Other part of sparc, IO, MMU, BUS IO, etc. Can run with low-voltage, shut-down to save power

## Slide 4
Domain | Voltage | Primary Power Net | Primary Ground Net | Always On?
pd_low (sparc, top-level) | 0.9V | VDD | VSS | No
pd_low_aon (lsu, tlu, ifu/ict, in-port) | 0.9V | VDD_AON | VSS | Yes
pd_hi (spu, ffu) | 1.6V | VDDH | VSS | No
pd_hi_aon (exu, out-port） | 1.6V | VDDH_AON | VSS | Yes
Sparc processor
lsu
tlu
ifu
ict
spu
ffu
exu
…
Locig view (i.e., verilog netlist)
Physical View
Load/save, instruction cache
Related, low voltage AO
Input Port is AO
lsu
tlu
exu

## Slide 5
Domain | Voltage | Primary Power Net | Primary Ground Net | Always On?
pd_low (sparc, top-level) | 0.9V | VDD | VSS | No
pd_low_aon (lsu, tlu, ifu/ict, in-port) | 0.9V | VDD_AON | VSS | Yes
pd_hi (spu, ffu) | 1.6V | VDDH | VSS | No
pd_hi_aon (exu, out-port） | 1.6V | VDDH_AON | VSS | Yes
Sparc processor
lsu
tlu
ifu
ict
spu
ffu
exu
…
Locig view (i.e., verilog netlist)
Physical View
i.e. ALU uses high voltage
For high-speed
FPU for floating point
Calculation. High volt.
Can be shut-down
For some time
exu
spu
ffu
lsu
tlu
ict
lsu
tlu
sparc
Load/save, instruction cache
Related, low voltage AO
Input Port is AO

## Slide 6
The challenge
Verilog module “usually” does not have power port
Have no idea on shut-down logic
How to communicate between two power domain
Physical implementation
The solution
Assign logic power domain to verilog module
Link module with target library
Add power port to verilog module
Create voltage region, connect with power network
Add inter-power-domain cells (ipd cell, power management cell)

## Slide 7
Define power domain
Link with target library
Add power port
Voltage region
Power network
Add IPD rule and cells
Check power domain
spu
ffu
For high voltage AO Cells.
Power domain
Same power
Strategy/ level/plan/ status
High-volt. VDD port
High-volt. VSS port
exu
spu
ffu
lsu
tlu
ict
lsu
tlu
sparc
Logical implementation
Physical implementation

## Slide 8
Low power background story
Low power 1: the logical diagram, power domain
Low power 2: the physical implementation
floorplan
power net, power region
power management cell
Low power 3: design rule check
UPF support
Agenda

## Slide 9
Define power domain
Link with target library
Add power port
Voltage region
Power network
Add IPD rule and cells
Check power domain
spu
ffu
Power domain defination example
create_supply_net VDD
set_power_domain pd_low -voltage 1.6 \
-primary_power_net VDD -primary_ground_net VSS -can_shutoff
assign_power_domain pd_low {spu ffu}
set_link_path -instance spu {tsmc160g-slow.lib ipd_slow.lib aobufx10-slow.lib}
create_supply_port VDD -domain pd_low
connect_power_domain_supply -force
Detailed example in lab 1 and lab 3:
/home/stor19d2p1/jchen2/newhire_training/lab/MVDD_labs/
  save/final-scripts/run-full.tcl, power_domain.tcl
module spu (… VDD_H_AO, VSS_HAO)

## Slide 10
Task 1:
Go to visit training lab, then create regression case to
create power domain
add power port
check result with report_power_domain
check power net connection
Futrher task:
create nested power domain
(a child-PD inside parent-PD)
combination with AO and shut-down PD

## Slide 11
Low power background story
Low power 1: the logical diagram, power domain
Low power 2: the physical implementation
floorplan
power network, power region
power management cell
Low power 3: design rule check
UPF support
Agenda

## Slide 12
Low power physical implementation : floorplan
There are three floorplan methods: (See lab 2 for details.)
  set_cell_boundary
    Physical region for one module instance
    Can be made into a partition (sub-project)
  set_place_group
    Physical region for multiple module instance
  add_island
  For always-on purposes
    Restrictions can be placed by cell type
      Level shifters
      Isolation cells
      Top level always on buffering
    Associated with power domain
Power domain cells will be placed in a physical region. (Placement engine handle it)
These regions are exclusive regions
(e.g. spu cells can NOT place into exu region,
exu cells can NOT place outside exu region)

## Slide 13
Why alway-on island?
Always-on
Power region
Always-on
Power region
Shut-down power region
Too long signal net, timing violation
island
Reduced
Timing delay
ff
For feedthrough buffing
For retention registers in shut-down region
For level-shifter, isolation cell placement

## Slide 14
Task 2:
Go to visit training lab 2, then create regression case to replace GUI procedure
  set_cell_boundary
  set_place_group
  add_island
Futrher task:
Test different geometory.
Can we create AO region inside another region?
If two regions overlapped, what will happen?
Can placer violate region constraint?
(place_cell)
For one power domain, can we create two islands?

## Slide 15
Low power physical implementation : power net
* Check /home/stor19d2p1/jchen2/QA_designs_v2/ARM_tiny_case/tiny_arm_pg.tcl
VDD
VSS
Suppose power port is created (in previous create_supply_port)
Suppose power net is defined (in previous create_supply_net)
Assign physical location of supply port (pad, bump location):
add_supply_locations -net VDD -metal 6 "14.54 22.53"
add_supply_locations -net VSS -metal 6 "24.188 25.03"
Logically connect net with port:
connect_global_net VDD -usage power -pin_pattern VDD
connect_global_net VSS -usage ground -pin_pattern VSS
tie_constant_pins -logic_0 VSS -logic_1 VDD
Pad/bump location

## Slide 16
Low power physical implementation : power network
ring
Manually create physical power network.
Power ring
set_param_ring pg_ring -layer M5
Power stripe
set_param_stripe s51 -ori V -layer M5
Power rail
set_param_rail r1 -ori H -layer M1
Execute power routing
complete_param_route
Connect cell pg with power network (suppose you added new cell or module
connect_global_net VDD -usage power -pin_pattern VDD
strap
stripe
* Check lab 4, power_mesh.tcl

## Slide 17
Task 3:
Go to visit training lab 4, source power_mesh.tcl
Create regression case by check the result of “list_param -detail”
Futrher task:
Modify the power network (set_param_*)
i.e., if stripe is narrow, shall result in larger IR drop

## Slide 18
Power management cell (ipd)
Where are we?
Defined power domains for each module.
Library is associated with each power domain
Power port and net are defined, placed.
Cells are placed in power region
Power network are created for each power region
What is the next?
communicate between power domain/region
preserve data during shut-down
turn-on turn-off power
clamp signal value after shut-down
Requires power management cell and rule
(ipd cells in GIGA)

## Slide 19
Shut-down power region
ff
x
ISO
Always-on
0.9 V
Always-on
1.6 V
LS
AO
Requires power management cell and rule
(ipd cells in GIGA)
Always-on
1.6 V
Isolation cell
Clamp signal
From shut-down
VDD
Virtual VDD
On/off
Power switch
Level shifter
Shift voltage
Retention FF
Preserve value
Always-On
Cell

## Slide 26
Power management cell (ipd) GIGA solution 1
set_ipd_rule
set_isolation_cell_rule
set_level_shifter_rule
set_retention_rule
insert_ipd_cells
Check_power_domain
Check lab 5 for details
connect_power_domain_supply
Check_power_domain
From domain A
To domain B
Use lib C
Control signal D

## Slide 27
add_power_switch_cell
connect_power_switch_cell
connect_global_net
Power management cell (ipd) GIGA solution 2
Power switches, power gating, MTCMOS
Check lab 1 and 2 for details

## Slide 28
Task 4:
Go to visit training lab 5, create regression case to cover insert_ipd_cell
And power switch cells.
We will talk about pst, upf next time.

## Slide 29
Low power background story
Low power 1: the logical diagram, power domain
Low power 2: the physical implementation
floorplan
power network, power region
power management cell
Low power 3: design rule check
UPF support
Agenda

## Slide 30
Reference:
Training lab location:
/home/stor19d2p1/jchen2/newhire_training/lab/MVDD_labs/
IEEE1801 UPF A brief introduction and overview, John Biggs
OpenSPARC™ T2 Core Microarchitecture Specification
Aguda User Guide
http://172.168.8.15:8088/projects/vulcanpower/wiki/Low_power_design_flow_and_training
http://172.168.8.15:8088/projects/vulcanpower/wiki/New_hire_training